## Slide 1
Aims and scope
Design a neutron source from synchrotron radiation and we want to investigate its feasibility in power production AND other applications
First attempt: too early
Subcritical reactor design (thermal)

## Slide 2
Aims and scope
Design a neutron source from synchrotron radiation and we want to investigate its feasibility in power production AND other applications
Roadmap
Do we have versatile and verified tools for the post-accelerator simulations?
Quantification of the synchrotron advantages in these kind of setups
Design of the subcritical ADS
Other applications?
First attempt: too early
 In these months we aimed at a solid foundation of the problem
Subcritical reactor design (thermal)

## Slide 3
Roadmap
Verification of OpenMC with MCNP and FLUKA
Subcritical reactor design (thermal)
PHYSOR 2026
1) Do we have versatile and verified tools for the post-accelerator simulations?
First attempt: too early
 In these months we aimed at a solid foundation of the problem

## Slide 4
 | Eigenvalue mode (keff) | Fixed source mode (power) | With Photonuclear | Possible improvements
 |  |  |  | -
X
X
X
X
Modified FLUKA version that accounts for keff: FLUKeff, developed at Polimi in 2023. We have the source code and parallel calculations are planned
Branch under development by a user on Github (@GuySten). The branch is available and we made a preliminary verification with this new OpenMC version
Post-accelerator simulation framework

## Slide 5
Verification of OpenMC with MCNP and FLUKA
PHYSOR 2026
Do we have faster and verified tools for the post-accelerator simulations?
monoenergetic
photons
photoneutrons
Broomstick problem
Comparison of photonuclear reaction rates and photoneutron energy distribution

## Slide 6
Verification of OpenMC with MCNP and FLUKA
PHYSOR 2026
Do we have faster and verified tools for the post-accelerator simulations?
photoneutrons
Broomstick problem
Comparison of photonuclear reaction rates and photoneutron energy distribution
- Good agreement within the three codes

## Slide 7
Verification of OpenMC with MCNP and FLUKA
PHYSOR 2026
Do we have faster and verified tools for the post-accelerator simulations?
photoneutrons
Broomstick problem
Comparison of photonuclear reaction rates and photoneutron energy distribution
Total number of photoneutrons ok, but:
- FLUKA better models the three body kinematic within n and alphas

## Slide 8
Verification of OpenMC with MCNP and FLUKA
PHYSOR 2026
Do we have faster and verified tools for the post-accelerator simulations?
photoneutrons
Broomstick problem
Comparison of photonuclear reaction rates and photoneutron energy distribution
Total number of photoneutrons ok. Difference in
Energy distribution problem: MCNP does not considers the kinematic in the laboratory frame
Mean value problem : reported bug within the nuclear library data
Correct mean value
Correct shape

## Slide 9
Bias in the photonuclear libraries
Nuclear data problems:
Bug with the code that process them (NJOY)
Wrong data with respect to experiments
 Systematic underestimation of MC codes in photoneutorn yields

## Slide 10
Bias in the photonuclear libraries
Case: electrons on tungsten
Same library
Same code

## Slide 11
Bias in the photonuclear libraries
There was also a validation.
Simulation predicts half of the interactions with respect to the experiment!!
We are in contact with the authors, asking for communications about the U238 data

## Slide 12
Bias in the photonuclear libraries
There was also a validation.
Simulation predicts half of the interactions with respect to the experiment!!
We are in contact with the authors, asking for communications about the U238 data
We can conclude that the photonuclear capabilities of OpenMC are verified : the code is able to simulate always the same number of photoneutrons as MCNP/FLUKA (with some caveats in the energy distribution)

## Slide 13
Verification of OpenMC with MCNP and FLUKA
Target optimization and justification for synchrotron usage
Subcritical reactor design (thermal)
Other applications: BNCT, etc..
PHYSOR 2026
PHYSOR 2026 (only OpenMC)
1) Do we have versatile and verified tools for the post-accelerator simulations?
Journal (FLUKA+MCNP, more results, more context)
2) Why do we want to use a synchrotron? Need for quantitative justification!
Roadmap

## Slide 14
Target optimization and justification for synchrotron usage
PHYSOR 2026 (only OpenMC)
Why do we want to use a synchrotron? Need for quantitative justification!

## Slide 15
Target optimization and justification for synchrotron usage
PHYSOR 2026 (only OpenMC)
Why do we want to use a synchrotron? Need for quantitative justification!
TAILORED case
EXPANDED case

## Slide 16
Target optimization and justification for synchrotron usage
PHYSOR 2026 (only OpenMC)
Why do we want to use a synchrotron? Need for quantitative justification!

## Slide 17
Target optimization and justification for synchrotron usage
PHYSOR 2026 (only OpenMC)
Why do we want to use a synchrotron? Need for quantitative justification!
Some random cases were also simulated in FLUKA to have a parallel confirmation of the results

## Slide 18
Target optimization and justification for synchrotron usage
PHYSOR 2026 (only OpenMC)
Why do we want to use a synchrotron? Need for quantitative justification!
Highlights:
Synchrotron’s photoneutron yield is higher than LINAC’s photoneutron yield (at their maximum reasonable power)
Synchrotron remove the problems related to the e-gamma interactions in the target
Synchrotron may exploit multiplexity (multiple beamlines)

## Slide 19
Target optimization and justification for synchrotron usage
Journal (FLUKA+MCNP, more results, more context)
Why do we want to use a synchrotron? Need for quantitative justification!

## Slide 20
Roadmap
Verification of OpenMC with MCNP and FLUKA
Target optimization and justification for synchrotron usage
Subcritical reactor design (thermal)
Other applications: BNCT, etc..
Subcritical reactor design (fast)
PHYSOR 2026
PHYSOR 2026 (only OpenMC)
1) Do we have versatile and verified tools for the post-accelerator simulations?
Journal (FLUKA+MCNP, more results, more context)
2) Why do we want to use a synchrotron? Need for quantitative justification!
k-eff limits
Other designs
PRELIMINARY
3) A lot of case tested, a couple show COP around 6

## Slide 21
Roadmap
Verification of OpenMC with MCNP and FLUKA
Target optimization and justification for synchrotron usage
Subcritical reactor design (thermal)
Other applications: BNCT, etc..
Subcritical reactor design (fast)
PHYSOR 2026
PHYSOR 2026 (only OpenMC)
Journal (FLUKA+MCNP, more results, more context)
k-eff limits
Other designs
Next steps:
Finalization of the thermal ADS design (different coolant and fuel tested: some cases showed a COP around 6) in stationary condition
For how much time the thermal ADS may operate withoout refuelling?
Evaluation of transient accidental scenarios
…

## Slide 22
Polimi manpower
Antonio Cammi – Full Professor
Carolina Introini – Postdoc
Lorenzo Loi – 3° year PhD
Andrea Missaglia - 3° year PhD
Arianna Iorio – MSc student
Riccardo Bossi - MSc student